# ME 639				Midterm Exam

- (20 Points) Consider the turbulent flow of an incompressible fluid.  Estimate the order of magnitude of the following quantities in terms of u, λ, and Λ:

- (30 Points) The equations for hear and mass transfer are given as

,

Here  is the diffusivity which is assumed to the same for heat and mass.  Derive the transport equations for the fluctuation temperature, T’, and fluctuation concentration C’.   Evaluate temperature-concentration correlation,.   Assume the fluid is incompressible.  Identify the terms corresponding to production, dissipation, diffusion and convection.  Find the order of magnitude of different terms.

- (25 Points) For a laminar boundary layer flow over a flat plate, obtain the variations of Us and  with x.  The governing equation are

4.	(25 Points) For stirring a cup of coffee with a 1 cm spoon requires a power of 0.0005 Watts.  Given that the mass of the coffee is 0.05 kg and the kinematic viscosity of water (coffee) is , estimate the Kolmogorov length and time scales, the turbulence fluctuation energy and time scale as well as the Taylor scale in the cup.